| ILLUSTRATED REPORT FOR BRILLIANT |  |  | Parameter | Avg | Min | Max | Dev | Cut | Sym |  |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Polished Brilliant | 02.08.2008 |  |  | Diameter, mm | 5.812 | 5.804 | 5.821 | 0.29% | E | EX |  |  | 5.813 | 5.815 | 5.810 | 5.811 |  |  |  |  |
|  |  |  |  | Crown angle, ° | 39.05 | 38.91 | 39.17 | 0.26 | Grading | EX |  |  | 39.08 | 38.91 | 38.99 | 39.09 | 39.12 | 39.17 | 39.10 | 38.92 |
|  |  |  |  | Pavilion angle, ° | 39.98 | 39.84 | 40.17 | 0.32 | Grading | EX |  |  | 39.99 | 40.12 | 40.17 | 39.97 | 39.91 | 39.84 | 39.87 | 39.95 |
| Model | Simple |  |  | Total height, % | 60.53 |  |  |  | E |  |  |  |  |  |  |  |  |  |  |  |
| Expert name | Makoed A.G. |  |  | Crown height, % | 15.88 | 15.79 | 16.06 | 0.28 | E | EX |  |  | 16.06 | 15.80 | 15.79 | 15.79 | 15.89 | 15.93 | 15.91 | 15.89 |
| Real weight, ct |  |  |  | Pavilion depth, % | 41.74 | 41.64 | 41.83 | 0.20 | N/A | EX |  |  | 41.64 | 41.73 | 41.76 | 41.72 | 41.83 | 41.76 | 41.82 | 41.66 |
| Calculated weight, ct | 0.74, 0.7431 |  |  | Table, % | 60.95 | 60.78 | 61.05 | 0.27 | Grading | EX |  |  | 60.78 | 60.99 | 61.05 | 60.98 |  |  |  |  |
| Measurements | 5.812 (5.804 -5.821) x 3.518 /0.010 mm |  |  | Culet, % | 0.39 | 0.33 | 0.41 | 0.08 | E | EX |  |  |  |  |  |  |  |  |  |  |
| Spread | -0.01 ct, -1.78 % |  |  | Girdle Bezel, % | 2.90 | 2.78 | 3.02 | 0.25 | E | EX |  |  | 2.83 | 2.99 | 2.98 | 3.02 | 2.80 | 2.84 | 2.78 | 2.97 |
| AGS Spread | N/A ct, N/A % |  |  | Girdle Bone, % | 2.85 | 2.65 | 3.09 | 0.44 |  | EX |  |  | 2.80 | 3.05 | 2.79 | 2.65 | 3.07 | 2.66 | 2.71 | 3.09 |
| Extra Facet / Nat | No |  |  | Girdle Valley, % | 0.95 | 0.72 | 1.17 | 0.45 | E | EX |  |  | 0.72 | 0.96 | 0.95 | 1.17 | 1.09 | 1.16 | 0.87 | 0.85 |
|  |  |  |  |  |  |  |  |  |  |  |  |  | 0.92 | 1.03 | 0.86 | 0.88 | 0.93 | 0.79 | 1.02 | 1.00 |
| Width | Length | Ratio (L/W) | Diameter Minimum | Diameter Maximum | Diameter Average | Total height |  |  | Star: | 61.69: | 60.59: | 63.53: | 2.94 | E | VG |  |  | 61.80: | 62.10: | 61.24: | 61.25: | 63.53: | 60.98: | 60.59: | 62.01: |
|  |  |  |  |  |  |  |  |  | Upper ratio, % | 38.31 | 39.41 | 36.47 |  |  |  |  |  | 38.20 | 37.90 | 38.76 | 38.75 | 36.47 | 39.02 | 39.41 | 37.99 |
| 5.804 mm | 5.821 mm | 1.003 | 5.804 mm | 5.821 mm | 5.812 mm | 3.518 mm |  |  | Star angle, ° | 25.81 | 25.56 | 26.10 | 0.53 |  | EX |  |  | 25.87 | 25.98 | 25.63 | 25.76 | 26.10 | 25.78 | 25.78 | 25.56 |
|  |  |  |  |  |  |  |  |  | Upper girdle angle, ° | 49.00 | 48.50 | 49.42 | 0.92 |  | EX |  |  | 48.80 | 49.28 | 48.64 | 48.50 | 49.01 | 49.21 | 48.74 | 49.06 |
|  |  |  |  |  |  |  |  |  |  |  |  | 49.09 | 49.25 | 48.89 | 49.06 | 48.95 | 48.98 | 49.42 | 49.06 |
| Crown height | Pavilion depth | Table | Culet | Girdle |  |  | Length girdle facet, % | 80.46 | 78.99 | 81.69 | 2.70 | E | EX |  |  | 79.58 | 80.42 | 80.34 | 80.78 | 80.85 | 81.34 | 80.94 | 81.69 |
|  |  |  |  | Bezel | Bone | Valley |  |  |  |  |  |  |  |  |  |  |  | 81.51 | 81.17 | 81.49 | 80.19 | 79.68 | 79.09 | 79.23 | 78.99 |
| 0.923 mm | 2.426 mm | 3.542 mm | 0.022 mm | 0.169 mm | 0.166 mm | 0.055 mm |  |  | Lower girdle angle / Halves angle, ° | 41.05 | 40.87 | 41.34 | 0.47 |  | EX |  |  | 41.16 | 41.13 | 41.34 | 41.26 | 41.14 | 41.01 | 41.01 | 40.94 |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 40.97 | 40.87 | 40.90 | 40.88 | 41.01 | 41.06 | 41.07 | 41.06 |
|  |  |  | Twist, ° | 0.81 | 0.20 | 1.46 | 1.26 |  | VG |  |  | 0.46 | 0.78 | 0.48 | 0.56 | 1.28 | 1.22 | 1.46 | 0.20 |
|  |  |  |  | Crown height, mm | 0.923 | 0.917 | 0.934 | 0.016 | E | EX |  |  | 0.934 | 0.918 | 0.917 | 0.918 | 0.924 | 0.926 | 0.924 | 0.923 |
|  |  |  |  | Pavilion depth, mm | 2.426 | 2.420 | 2.431 | 0.012 | N/A | EX |  |  | 2.420 | 2.425 | 2.427 | 2.424 | 2.431 | 2.427 | 2.430 | 2.421 |
|  |  |  |  | Table, mm | 3.542 | 3.532 | 3.548 | 0.016 | Grading | EX |  |  | 3.532 | 3.544 | 3.548 | 3.544 |  |  |  |  |
|  |  |  |  | Culet, mm | 0.022 | 0.019 | 0.024 | 0.005 | E | EX |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  | Girdle Bezel, mm | 0.169 | 0.161 | 0.176 | 0.014 | E | EX |  |  | 0.164 | 0.174 | 0.173 | 0.176 | 0.163 | 0.165 | 0.161 | 0.173 |
|  |  |  |  | Girdle Bone, mm | 0.166 | 0.154 | 0.180 | 0.026 |  | EX |  |  | 0.163 | 0.177 | 0.162 | 0.154 | 0.179 | 0.155 | 0.158 | 0.180 |
|  |  |  |  | Girdle Valley, mm | 0.055 | 0.042 | 0.068 | 0.026 | E | EX |  |  | 0.042 | 0.056 | 0.055 | 0.068 | 0.063 | 0.068 | 0.050 | 0.050 |
|  |  |  |  |  |  |  |  |  |  |  |  |  | 0.053 | 0.060 | 0.050 | 0.051 | 0.054 | 0.046 | 0.059 | 0.058 |
|  |  |  |  | Measurement as per OctoNus theory: |  |  |  |
|  |  |  |  | Crown angle, ° | 39.05 | 39.01 | 39.10 | 0.10 |  |  |  |  | 39.10 | 39.04 | 39.05 | 39.01 |  |  |  |  |
|  |  |  |  | Pavilion angle, ° | 39.98 | 39.95 | 40.02 | 0.07 |  |  |  |  | 39.95 | 39.98 | 40.02 | 39.96 |  |  |  |  |
|  |  |  |  | Fish eye effect, ° | 2.47 | N/A |  |  |  | MIC, mm | 5.794 |
|  |  |  |  | Culet through Crown Bezel, ° | 7.91 | N/A |  |  |  | Girdle to MIC, mm | 0.010 |
|  |  |  |  | Parameter, ° | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  |  | Paint / Dug | Avg | Type | Sym | Dev | Sym |
|  |  |  |  | Pav. azimuths dev. from ideal | 0.00 | -0.56 | -0.10 | -0.15 | -0.65 | -0.74 | -0.83 | -0.05 |  |  | Crown, ° | 0.12 |  | EX | -0.97 | EX |
|  |  |  |  | Crown azimuths dev. from ideal | 0.46 | 0.22 | 0.38 | 0.41 | 0.63 | 0.48 | 0.64 | 0.16 |  |  | Crown, notch. | 0.0, Negligible |  |  | 0.3 |  |
|  |  |  |  | Crown painting | -0.61 | 0.89 | -0.49 | -0.71 | 0.34 | 0.72 | -0.50 | 0.81 |  |  | Pavilion, ° | 0.10 |  | EX | 1.17 | EX |
|  |  |  |  |  | -0.97 | 0.21 | -0.20 | 0.85 | -0.12 | 0.64 | 0.50 | 0.58 |  |  | Pavilion, notch. | 0.0, Negligible |  |  | 0.3 |  |
|  |  |  |  | Pavilion painting | -0.27 | -0.47 | 1.17 | -0.30 | 0.18 | -0.05 | 0.31 | -0.17 |  |  |  |
|  |  |  |  |  | 0.23 | -0.55 | 0.82 | -0.73 | 0.72 | 0.39 | -0.04 | 0.31 |  |  |  |
| Appraiser title | GIA_PCTG_StarCul |  |  |  |  |  |  |  |
| Overall cut quality | G |  |  |  |  |  |  |  |
| Symmetry appraiser title | Internal |  |  |  |  |  |  |  |
| Overall symmetry quality | VG |  |  |  |  |  |  |  |
| Color |  |  |  |  |  |  |  |  |
| Clarity |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | Girdle center |  | Culet center |  | Тable center |  |  |  |
| Polish |  |  |  | Girdle-Culet offset by table axis | 0.28 ± 0.22, % | 0.016 ± 0.013, mm |  |  |  |
|  |  |  |  | Girdle-Table offset by table axis | 0.10 ± 0.20, % | 0.006 ± 0.011, mm |  |  |  |
| Fluorescence |  |  |  | Table-Culet offset by table axis | 0.33 ± 0.23, % | 0.019 ± 0.014, mm |  |  |  |
|  |  |  |  | Girdle to table-culet line offset | 0.08 %, 0.005 mm |  |  |  |